## Slide 1: T29: Environment, Safety
Pedestrian dynamics
Alastair Shipman and Georgia Bateman

## Slide 2: Introduction
How do you design an Olympic village to accommodate 100,000 people. What happens if 200,000 turn up?
How do you future proof Crossrail for the increasing population of London?
What do you do in the zombie apocalypse? What do other people do?

## Slide 3: ILOs of this course
Define the topics of pedestrian and evacuation dynamics
Outline the main emergent properties of crowd behaviour
Employ the hydraulic model of evacuation
Outline the main theories of human behaviour in evacuations,
Recall and develop the different algorithms used for pedestrian dynamics simulation models.
Evaluate the design of experiments and data gathering

## Slide 4: History
In the 50s:
  Hankin, B.D. and R.A. Wright, Passenger Flow in Subways. Journal of the Operational Research Society
In the 70s and 80s:
  Fruin, Pedestrian planning and design. 1st ed. 1971
  Predtechenskii…
In the 90s:
  Helbing
In the 2000s:
  All sorts of rubbish
In the 10s:
  All more sorts of rubbish.

## Slide 5: Pedestrian dynamics models
Macro scale
Micro scale
Meso scale
Agent based
Fluid based
Cellular Automata
Network
Etc.

## Slide 6: Pedestrian dynamics: fundamental diagrams
Speed vs Density

## Slide 7: Pedestrian dynamics: fundamental diagrams
Flow vs Density

## Slide 8: Hydraulic model: introduction
This is a micro scale model: it looks at individual buildings.
It treats people as discrete groups, not individuals.
  Similar to fluid models, but simpler maths.
Based mostly on fundamental diagram

## Slide 9: Hydraulic model: fundamental diagrams

## Slide 10: Hydraulic model: introduction
Elements and transitions
Solve a quadratic in density either side of a transition
Use that density to solve for speed and flow rate.
That informs time taken for traversal
Finally, add up all the times taken to evacuate

## Slide 11: Hydraulic model: introduction
Elements and transitions
Solve a quadratic in density either side of a transition
Use that density to solve for speed and flow rate.
That informs time taken for traversal
Finally, add up all the times taken to evacuate

## Slide 12: Hydraulic model: introduction
Elements and transitions
Solve a quadratic in density either side of a transition
Use that density to solve for speed and flow rate.
That informs time taken for traversal
Finally, add up all the times taken to evacuate

## Slide 13: Hydraulic model: introduction
Elements and transitions
Solve a quadratic in density either side of a transition
Use that density to solve for speed and flow rate.
That informs time taken for traversal
Finally, add up all the times taken to evacuate

## Slide 14: Hydraulic model: introduction
Elements and transitions
Solve a quadratic in density either side of a transition
Use that density to solve for speed and flow rate.
That informs time taken for traversal
Finally, add up all the times taken to evacuate

## Slide 15: Hydraulic model: introduction
Elements and transitions
Solve a quadratic in density either side of a transition
Use that density to solve for speed and flow rate.
That informs time taken for traversal
Finally, add up all the times taken to evacuate

## Slide 16: Hydraulic model: equations
S=k-akD: constant for elements. A constant, k defined by element.
F= SDWe: We defined by element.
F= kD(a-kD)We: combining the above.
Fin=min(Fout, Fmax): limited at transition points.
Can use this to find out how long it takes to move through a building.

## Slide 17: Hydraulic model: Example
50 people
1.5ppl/m^2
Staircase
Length =3.3m
Width =1.8m
Corridor
Length =10m
Width =1.8m
Door
Width =1.8m

## Slide 18: Examples: videos
Insert massmotion, pathfinder, SIMULEX etc

## Slide 19: So what do we need to know to properly model this?
Data analysis and generation methods
Simulation
Psychology
Physiology: step length, fitness levels, typical anatomy and morphology. Density estimations.
Learning and cognitive processes
Building design and codes

## Slide 20: How can this help?
Influence new designs
Retrofit existing buildings
Support real-time decision making (especially in emergencies)

## Slide 21: Workshop: build fundamental diagram
Rope circle: 2m^2
3-8 people

## Slide 22: Workshop: Hydraulic model
Skempton building. How long does it take for this room to evacuate the building?
Assumptions:
  Rest of the building is empty
  All room occupants follow the same, shortest path
  All occupants follow standard speed/flow/density relationships
45 minutes, work in groups, present answers for 15 minutes.

## Slide 23: Mentimeter poll
The hydraulic model can accommodate different demographic characteristics: TRUE/FALSE
The hydraulic model is an agent based model: TRUE/FALSE
I want to look at the evacuation of a city, what type of model should I use: MACRO/MICRO/MESO

## Slide 24: Intro to remainder of course
Flipped approach
  Online lectures
    We will be releasing videos on blackboard. You need to watch these before turning up to the class
  Workshops
    Hand-on learning and practice of lecture material
Mentimeter quizzes
  They will cover the work done in the previous workshop, as well as the lectures you have watched.
  They will form part of your coursework mark.